BZJ.B series of Semi- automatic Flute Laminator

Main Characteristics:

- The machine adopt bottom paper vacuum style feeding, up paper manual feeding, easy operation, accuracy transmission, bottom and up paper adopt photoelectrical control, special front gauge fix position, bottom paper never go ahead.

- This machine pressure part adopt suspension lamination style, make the board uniform stress, steady feeding, making the board beautiful and smooth, stress belt can move front and behind, can be suitable to many kinds of paperboard in various size.

- Main parts of all the machine adopt the famous company original products, it have long service life and steady function.

Technical Parameters:

| Model | Max Paper Size | Min paper Size | Laminator precision | Max speed | Total power | Machine length | Total Weight |
| --- | --- | --- | --- | --- | --- | --- | --- |
| BZJ.B-1300S | 1300x1100 | 350x350 | ±1.5 | 0-60 | 5kw | 8 m | 3.5T |
| BZJ.B-1450S | 1450x1100 | 350x350 | ±1.5 | 0-60 | 5kw | 8 m | 3.5T |
| BZJ.B-1450L | 1450x1400 | 450x450 | ±1.5 | 0-60 | 5kw | 8 m | 3.5T |
| BZJ.B-1600L | 1600x1400 | 450x450 | ±1.5 | 0-60 | 5kw | 8 m | 3.5T |